## Slide 1
Mathematics of Glass
Part IV: Blow Process
Bob Mattheij, Hans Groot, Christina Giannopapa

## Slide 2: Overview
Introduction
Glass Blowing Simulation Model
Level Set Methods
Results
Some thoughts on inverse problem
Conclusions

## Slide 3: Glass Manufacturing
Glass Melting
Glass Conditioning
Automatic Inspection
Glass Forming
Surface Treatment

## Slide 4: Glass Forming
  press
  press-blow
  blow-blow

## Slide 5: Blow-Blow Process
glass
mould
ring
preform
mould
ring

## Slide 6: Blow Model
Flow of glass and air
  Stokes flow problem
    Viscous forces dominate
    Temperature dependent glass viscosity
Energy exchange in glass and air
  Convection diffusion
  problem
    No viscous dissipation
Evolution of glass-air interfaces
  Convection problem for level sets

## Slide 7
Level Set Method
glass
air
air
θ > 0
θ < 0
θ < 0
θ = 0
θ: level set function
  Initially defined as signed distance function:

## Slide 8
θ = 0
θ = distance
tnew
told
Level set Example

## Slide 9
Re-initialisation by FMM Algorithm I
Update The computed level set function at each time step so that
  position interface does not change
  length of gradient close to 1 within elements
  Convection causes gradient to become irregular after some time
Hence we have to re-initialisise as follows
Fast Marching Methods (FMM) (re)build the solution outward starting with a narrow band around interface

## Slide 10
proximate nodes: correct value by assumption
unidentified nodes: not yet considered
Interface
Re-initialisation by FMM Algorithm II

## Slide 11
proximate nodes: correct value by assumption
trial nodes: value might not be correct
unidentified nodes: not yet considered
Interface
Re-initialisation by FMM Algorithm III

## Slide 12
A
B
C
Compute trial value C from proximate values A and B and mesh size
Re-initialisation by FMM Algorithm IV

## Slide 13
C
B
A
Δx
Re-initialisation by FMM Algorithm V
This a quadratic equation in θC , which can simply be solved

## Slide 14
A
B
C
Trial point C is added to set of accepted points
Re-initialisation by FMM Algorithm VI

## Slide 15
proximate nodes: value correct by assumption
trial nodes: value might not be correct
accepted nodes: value updated by FMM
Re-initialisation by FMM Algorithm VII

## Slide 16
proximate nodes: value correct by assumption
trial nodes: value might not be correct
accepted nodes: value updated by FMM
Re-initialisation by FMM Algorithm VIII

## Slide 17
proximate nodes: value correct by assumption
trial nodes: value might not be correct
accepted nodes: value updated by FMM
Re-initialisation by FMM Algorithm IX

## Slide 18: Computer Simulation Model
Finite element discretization
One fixed mesh for entire flow domain
2D axi-symmetric
At equipment boundaries:
  no-slip of glass
  air is allowed to “flow out”
Preform
Bottle

## Slide 19: Simulation steps I
Notes: <number>
<footer>
<header>
<date/time>

## Slide 20
Preform Blowing Simulation
Temperature
Glass-air interface

## Slide 21
Bottle Blowing Simulation
Temperature
Glass-air interface

## Slide 22: Simulation steps I
Notes: <number>
<footer>
<header>
<date/time>

## Slide 23: Simulation steps III
Notes: <number>
<footer>
<header>
<date/time>

## Slide 24: Simulation steps IV
Notes: <number>
<footer>
<header>
<date/time>

## Slide 25
Volume Conservation
Euler Implicit with Δt = 1E-4