## Slide 1
Mathematics of Glass
Part VI: Conservation?
Bob Mattheij, Konstantin Laevsky, Bratislav Tasic

## Slide 2
On Numerical Volume Preservation of a Divergence
Free Fluid under Symmetry
OR…

## Slide 3
Motivation from an example in glass industry
Streamfunction and Hamiltonians
Example of 3D case with rotational symmetry
General formulation
Application to spherical coordinates with examples
Contents

## Slide 4
One of the basic laws in fluid mechanics is the
conservation of mass. Together with the momentum
equation it determines the motion of the fluid body.
In situations where we have an incompressible fluid
the mass conservation can be seen as an algebraic constraint
for the momentum equation. If we have a
moving boundary the actual position follows from
solving an ODE for the latter. This ODE still
requires the solution to satisfy the mass conservation
in a numerical simulation.
Mass Conservation ?

## Slide 5
Glass is pressed in a mould, through a so called plunger, which is moved upward by a piston to produce a parison.
The mould is first closed and then the plunger starts to move till it is
stopped by counter pressure or machine control. After this, some
further processing may be done to produce the wanted form.
In good approximation the problem is axisymmetric and thus
mathematically 2-dimensional
parison
(preform)
plunger
mould
neck
piston
gob
Example I

## Slide 6
Fp
Fg
Example II

## Slide 7
This problem can be modelled by a Stokes equation:
}
in
We need some proper boundary
conditions to have a complete
problem, like :
t
n
Here v is the velocity and p the pressure
Example III
r
z
t
free
boundary
symmetry boundary: free boundary:

## Slide 8
Stokes & evolution
As for the motion of the glass, we can model the flow by a
series of boundary value problems, where the evolution is
coming from a kinematic boundary condition imposed by the
plunger.
Note that this describes the displacement of all “points” in
the gob. We are particularly interested in the free boundary
The evolution equation is nothing but the “simple”ODE
plunger velocity
slip factor

## Slide 9
The Stokes problem can be solved in a straightforward manner
by a Finite Element Solver. What is left to do is to solve the
ODE for the position, given the velocity.
Note that only the free boundary is of interest.
Hence we may consider a Langrangian
displacement of a number of boundary
points (edges of the boundary elements),
e.g. through explicit Euler:
(n time level, i point)
This may result in displacements outside
the region .We just clip these points
(resulting in possible loss of mass)
Updating the Boundary
upper part
of glass body

## Slide 10
Approximating ODE
The most simple approximations of the ODE
are given by the Euler methods
Here h is the step size, t n=nh and x n  x(t n)
Typically, for we obtain
INTERMEZZO
……………………………………………………………..

## Slide 11
Stability I
Although the behaviour of the solution may (strongly) depend on
the source term g, the stability does not; we therefore investigate
how analytical stability properties are carried over to numerical
ones. In particular we may assume then the ODE to be homogeneous.
Of course this ODE is stable if λ < 0 and unstable if λ > 0.
Note that this means that
x(t n+1)/x(t n) = eh λ <1, if the ODE is stable
x(t n+1)/x(t n )= eh λ >1, if the ODE is unstable
Hence a numerical method should - ideally - have the property

## Slide 12
For the Euler methods we have
Note that both are O(h λ) approximations of e h λ, h λ  0.
One can draw so called stability regions  (GREEN)
+2
-2
END INTERMEZZO
………………………………………………………………..
Stability II

## Slide 13
We see that the volume is increasing, though less for smaller
stepsizes. But we do not want to take h extremely small unless the problem is very stiff (which it is not)
Mass Conservation?
For the plunger problem, solving the ODE by Euler explicit
gives for h= 0.01, 0.005 and 0.0025:

## Slide 14
Conservation
The continuity equation, which simply reads
implies that the mass (here the “volume”, since density has been
eliminated) is a conserved quantity. Another formulation of this
can be given in terms of stream functions as a Hamiltonian:
For simplicity we consider Cartesian co-ordinates:
So with
Define the “streamfunction” (the Hamiltonian)
Then

## Slide 15
This streamfunction  describes a flow with a constant volume.
This can be seen as follows: Let δ x and δ y be small perturbations of
x(t) and y(t) resp. Then
So
Note that the trace of this matrix H is zero. If dp:=
and dq another such vector, then vol:=det(dp|dq) satisfies
Volume Preservation I
NB:

## Slide 16
dp
dq
Hence det [dp|dq] is constant, although
it may deform in time
For a reasonable numerical method this conservation should
be taken into account. This gives rise to so called
symplectic integrators. Apparently we have
A simple example of such a method is the midpoint rule
Symplectic Integrators

## Slide 17
A perturbed recursion (“first variation”) will now look like
This can be written as
For infinitesimal volumes dpn and dqn we thus have
It is simple to see now that
so
Volume Preservation II

## Slide 18
INSTRUCTIVE EXAMPLE
In order to see what a numerical method may do to a conservative
problem, consider the following simple motion:
Note that is a conserved quantity, like the mass
(volume) in the glass. The phase plane portrait is a circle
with solution
Example
……………………………………………………………...

## Slide 19
Indeed,  is a Hamiltonian, as one can simply see
Hamiltonian

## Slide 20
Decoupled ODE

## Slide 21
-1.5
-1
-0.5
0
0.5
1
1.5
-1.5
-1
-0.5
0
0.5
1
1.5
-1.5
-1.5
-1
-0.5
0
0.5
1
1.5
-1
-0.5
0
0.5
1
1.5
Results of explicit Euler and implicit Euler, h=0.05.
With the midpoint rule we obtain a perfect circle.
Note that for an ODE like
we have
Hence , = 1, 0, ½

## Slide 22
We can easily see that this means, e.g. for the
explicit Euler formula
Apparently this grows exponentially in time, albeit with an
“exponent co-efficient” equal to the stepsize h
(Non) conservation

## Slide 23
Non-Mass Conservation
Recall the plunger problem, where the ODE was solved by
Euler explicit with h= 0.01, 0.005 and 0.0025:
This appears to be in line with the exponential growth predicted in the simple problem

## Slide 24
This method is simplectic
Simplecticity requires the problem to be of even order.
Hence we cannot directly use such a method for our flow
problem.
Below we investigate how we can still employ such methods
for three dimensional problems, if there exists some form of
symmetry. We shall deal with this question now for a
general flow problem having symmetry, i.e essentially being 2D
(Non) conservation
If we use the implicit midpoint rule then of course we would get
Though this method is implicit, we can use e.g. a predictor (e.g. Euler forward)-corrector scheme.

## Slide 25
To start with, consider a 3-D flow with rotational symmetry. We try
to reformulate the divergence equation, such that it is in Hamiltonian
form. Of course symmetry means that we have 2 independent variables..
Recalling the glass example shown before we first look at cylindrical
co-ordinates:

z
r
Cylinder co-ordinates I

## Slide 26
Then we obtain
In the axisymmetric case we clearly have
So a streamfunction, ψ , is defined by
Note that we have . ψ(r,z) is not a Hamiltonian
Cylinder co-ordinates II

## Slide 27
So ψ( ) is Hamiltonian system in the variables:
However, one can then simply check that
Cylinder co-ordinates III

## Slide 28
We shall give two examples showing how the midpoint
rule behaves under this transformation
Cylinder co-ordinates IV

## Slide 29
Example 1
Consider an axisymmetrical velocity field, given by
The solution is simply seen to be
If D(0) is a cylinder with radius r(0) and height z(0), we see that
the volume ½ r2(t)z(t) of the cylinder D(t) is constant. Note that
in (1) , so is not a Hamiltonian. However,
(1)
gives rise to a proper Hamiltonian form

## Slide 30
In other words
Example 1; ctd
Now if we would use the obvious form (1) , we find
Hence

## Slide 31
Example 1; ctd
In conservation form the ODE would rather read
For the conservative form we thus find

## Slide 32
Example 1; ctd
Hence
or

## Slide 33
Example 1 (midpoint simulation)

## Slide 34
In order to implement the midpoint rule we may employ
e.g. a predictor-corrector technique. Note that the problem is
not stiff. As predictor we use Euler forward. Per corrector step
the accuracy increases by about a factor h.
We have performed a number (m) of correction steps.
The graph below shows the numerically computed
volume of the cylinder for the simulation above.
Example 1 (midpoint simulation); ctd

## Slide 35
Example 1 (midpoint simulation); ctd
Volume error h=0.075 m=8
*10-14
Time 

## Slide 36
The second problem is nonlinear. Consider the velocity field
Using the transformation , we find
Clearly is a Hamiltonian!
In the next pictures we have computed the flow of a cylinder
which has initial height  and radius 1
Example 2

## Slide 37
Example 2 (midpoint simulation)

## Slide 38
Since we have a more complicated body we can only
use numerical tools to compute the volume of this
body. We have employed a trapezoidal rule for integration.
The number of points on the surface was quite high, viz. 104.
Of course this was only done to illustrate the accuracy of the
symplectic integration. Indeed the second order error of the
trap rule is the bottle neck for the accuracy!
Example 2 (midpoint simulation)

## Slide 39
*10-9
Volume h=0.075 m=8
Example 2 (midpoint simulation)

## Slide 40
General orthogonal systems I
For a general orthogonal system, with variables say α, β, γ and their corresponding scaling factors h1, h2, h3, we find
the following: with etc and

## Slide 41
Let e.g. and let the scaling be separable, i.e.
then we apparently have
By defining
we find
where
General orthogonal systems II

## Slide 42
Assuming that F(α) and G(β) are invertible, we thus find the following conservation form
General orthogonal systems III

## Slide 43
In spherical co-ordinates we have
ϕ
ϑ
r
Just to illustrate the main point, viz. the 2-D necessity, we first
consider the motion on the sphere (i.e. a 2-dimensional flow),
say with r=1. Then we obtain for the stream function
Since we obtain
Spherical co-ordinates

## Slide 44
a stream function, given by
Clearly α= θ, β = φ. And we have h1=1, h2 = sin θ
Spherical co-ordinates
Hence we take f(x)=sin θ and g(y)= φ.

## Slide 45
Example 3 (sphere)
In the next example we have taken a patch on a sphere
and computed the motion based on the transformations
above, employing the midpoint rule. For illustrative
purposes w also display the results for forward and
backward Euler

## Slide 46
Explicit
Implicit
Midpoint
Example 3 (sphere)

## Slide 47
If the flow is 3-D but axisymmetric we find
So the stream function satisfies
One can work this out to obtain
Obviously we can choose
Spherical co-ordinates; axisymmetry

## Slide 48
A well known example is slow flow past a sphere with radius 1,
This problem can be solved exactly when we assume that the
problem can be described by a Stokes equation. The result can
be expressed using the stream function, given by
The velocity components are
Example 4 (Stokes)

## Slide 49
Example 4 (Stokes)

## Slide 50
It is possible to employ simplectic methods for 3-D problems when they have some form of symmetry
The midpoint rule is just one example. It is implicit and therefore requires extra effort
Remark:
It is possible to bypass the latter problem is the velocity field is autonomous. In practice this is also fine for problems where the time dependency is very small. This gives rise to so called flow methods
Conclusions

## Slide 51
Thus far we assumed that the velocity field was given explicitly.
One should note that this was necessary in order to use
implicit methods. In practice we have at best a numerically
determined velocity field. However, since the ODE is
autonomous, we can get around this inherent problem
by employing the flow information of previous time steps
for subsequent ones.

## Slide 53
ellipse linear
ellipse quadratic

## Slide 54
stokes linear
stokes quadratic